## Slide 1: TiGL Workshop
Curve Network Interpolation with Gordon Surfaces
12.09.2018
Merlin Pelz
System Dynamics and Control | SR-FLS
DLR Oberpfaffenhofen

## Slide 2: Curve Network Interpolation with Gordon Surfaces

## Slide 3: The Curve Network Interpolation Problem
Definition of the problem:
  Given a network of profile and guide curves, find surface(s) which interpolate(s) these curves
guides
profiles
example of a curve network

## Slide 4: Why Gordon Surfaces? Problems with Old Method
In Digital-X, Open CASCADE was contracted for the implementation of this algorithm (based on Coons Patches)
Problems from aero simulations:
  Pressure oscillations on the wing
  Surface modelling probably the issue!
Analysis:
  Generated surfaces have small bumps, waves and kinks
  The latter is caused by C1 or C2 discontinuities on the surface
Conclusion:
  Must implement a better algorithm by our own: Gordon Surfaces

## Slide 6: B-splines

## Slide 7: B-splines
Definition: A B-spline curve of order (and degree ) is defined as
with its control points and basis functions of order .
Specify a knot vector where for all .
Then:

## Slide 8: B-splines
Definition: A B-spline curve of order (and degree ) is defined as
with its control points and basis functions of order .
Specify a knot vector where for all .
Then:
Definition:- uniform knot vector: for all : , non-uniform otherwise
- clamped knot vector: for all :
(endpoint interpolation) for all :

## Slide 9: B-splines
Some other properties: - for all (locality)
- is -continuous
-
- convex hull property

## Slide 10: B-splines
Some other properties: - for all (locality)
- is -continuous
-
- convex hull property
Changing the shape of a B-spline curve by:
moving the control points

## Slide 11: B-splines
Some other properties: - for all (locality)
- is -continuous
-
- convex hull property
Changing the shape of a B-spline curve by:
moving the control points
adding/removing control points

## Slide 12: B-splines
Some other properties: - for all (locality)
- is -continuous
-
- convex hull property
Changing the shape of a B-spline curve by:
moving the control points
adding/removing control points
closer to/farther from the point

## Slide 13: B-splines
Some other properties: - for all (locality)
- is -continuous
-
- convex hull property
Changing the shape of a B-spline curve by:
moving the control points
adding/removing control points
closer to/farther from the point
- using multiple control points

## Slide 14: B-splines
Some other properties: - for all (locality)
- is -continuous
-
- convex hull property
Changing the shape of a B-spline curve by:
moving the control points
adding/removing control points
closer to/farther from the point
- using multiple control points
changing the order of

## Slide 15: B-splines
Some other properties: - for all (locality)
- is -continuous
-
- convex hull property
Changing the shape of a B-spline curve by:
moving the control points
adding/removing control points
closer to/farther from the point
- using multiple control points
changing the order of
smoother and less close to the control polygon for bigger

## Slide 16: B-splines
Some other properties: - for all (locality)
- is -continuous
-
- convex hull property
Changing the shape of a B-spline curve by:
moving the control points
adding/removing control points
closer to/farther from the point
- using multiple control points
changing the order of
smoother and less close to the control polygon for bigger
using multiple knots

## Slide 17: B-splines
Some other properties: - for all (locality)
- is -continuous
-
- convex hull property
Changing the shape of a B-spline curve by:
moving the control points
adding/removing control points
closer to/farther from the point
- using multiple control points
changing the order of
smoother and less close to the control polygon for bigger
using multiple knots
clamped curve
for knot multiplicity : curve is -continuous at the corresp. point

## Slide 18: B-splines
Some other properties: - for all (locality)
- is -continuous
-
- convex hull property
Changing the shape of a B-spline curve by:
moving the control points
adding/removing control points
closer to/farther from the point
- using multiple control points
changing the order of
smoother and less close to the control polygon for bigger
using multiple knots
clamped curve
for knot multiplicity : curve is -continuous at the corresp. point
changing the relative spacing of the knots

## Slide 19: B-splines
Some other properties: - for all (locality)
- is -continuous
-
- convex hull property
Changing the shape of a B-spline curve by:
moving the control points
adding/removing control points
closer to/farther from the point
- using multiple control points
changing the order of
smoother and less close to the control polygon for bigger
using multiple knots
clamped curve
for knot multiplicity : curve is -continuous at the corresp. point
changing the relative spacing of the knots
closer knots: curve moves closer to corresponding control point

## Slide 20: B-splines
Default setting: - cubic:
- no multiple control points
Remarks: - Beziér curve for and no internal knots
- closed curve defined by the points :
control points:
- B-spline surface, also called patch:
, ,

## Slide 21: Mathematical Theory of Gordon Surfaces

## Slide 22: Gordon Surfaces

## Slide 23: Steps for Creating the Gordon Surface in Detail

## Slide 24: Main Steps
Reparametrization of B-spline curves
Creating a common knot vector for B-spline curves and surfaces
  Degree elevation for B-spline curves and surfaces
  Knot insertion for B-spline curves and surfaces
Finding the intersection points of the curve network
Creating the two skinned surfaces
Creating tensor product surface
Creating the Gordon Surface

## Slide 25: -Continuous B-spline Curve Reparametrization
Problem:
    Make curve network compatible for the Gordon Surface theory
    Therefore: reparametrize every curve by giving certain new parameter values for all -directional and all -directional curves at their intersection parameter values
So, find such that

## Slide 26: -Continuous B-spline Curve Reparametrization
Compute sample points on the curve
Interpolate these points at new parameter values by a B-spline curve such that:

## Slide 27: -Continuous B-spline Curve Reparametrization
Compute sample points on the curve
Interpolate these points at new parameter values by a B-spline curve such that:
The approximation by is done for not having to
elevate the degree of the input curve
Higher degree of B-spline curve ~ lower efficiency for
computations
Picture: example of a compatible curve network for a wing
of an airplane after reparametrization

## Slide 28: Creating a Common Knot Vector
Problem: all B-spline curves and surfaces shall have the same knot vector
In case of curves:
    Create a vector of all unique knots of all curves
    Create a vector of the multiplicities of each knot in
    Insert as many knots as needed in all knot vectors to get the vector with multiplicities
For surfaces, do this with both knot vectors and

## Slide 29: Creating the Skinned Surfaces
Problem: skin all -directional curves of the curve network
Write all control points of all B-spline curves in a matrix
Interpolate control points by -directional B-spline curves at certain parameter values to get :
Create skinned surface with control points , knot vectors and degrees of -directional and -directional B-spline curves

## Slide 30: Creating the Skinned Surfaces
Problem: skin all the -directional B-spline curves
Use the same method as before and flip the parameters and of the surface to get
Create the skinned surface by transposing the control point matrix, using the knot vector for and vice versa, and the -directional degree for the -directional degree and vice versa

## Slide 31: Creating the Tensor Product Surface
Problem: create intersection points interpolating tensor product surface
Find the intersection points of the curve network
Interpolate all the points by -directional B-spline curves at certain parameter values :
Create a skinned surface with these curves

## Slide 32: Finally: Creating the Gordon Surface
Making the curve network compatible by reparametrization
Get common degree and knot vector of the curves in the two directions
Find the intersection points and their parameters
Create the two skinned surfaces with these parameters
Create the tensor product surface with these parameters
Create common knot vector for these three surfaces
Create B-spline Gordon Surface by superposing the corresponding control points of the three surfaces (this way B-spline surfaces are superposed)

## Slide 33: Results

## Slide 34: Zebra Stripe Plot
Surface quality analysis with zebra stripe plot (in TiGL Viewer 3)

## Slide 35: Gordon Surfaces: Results for a Nacelle

## Slide 36: Gordon Surfaces: Results for a Wing

## Slide 37: Gordon Surfaces: Results for a General Surface

## Slide 38: Comparison of Coons and Gordon: Nacelle
Coons Patches
Gordon Surface
(one half of the same nacelle)

## Slide 39: Comparison of Coons and Gordon: Nacelle
Coons Patches
Gordon Surface

## Slide 40: Comparison of Coons and Gordon: Nacelle
Coons Patches
Gordon Surface

## Slide 41: Comparison of Coons and Gordon: Wing
Coons Patches
Gordon Surface

## Slide 42: Comparison of Coons and Gordon: Wing
Coons Patches

## Slide 43: Comparison of Coons and Gordon: Wing
Gordon Surface

## Slide 44: Comparison of Coons and Gordon: Wing
Coons Patches
Gordon Surface

## Slide 45: Comparison of Coons and Gordon: General Surface
Coons Patches
Gordon Surface

## Slide 46: Comparison of Coons and Gordon: General Surface
Coons Patches
Gordon Surface

## Slide 47: Summary

## Slide 48: Summary
Gordon Surface method was presented
Curve reparametrization is crucial→ compatible curve network
Results:
  all the previous problems are eliminated now
  but: because of global interpolation oscillations might occur
  solution: different reparametrization

## Slide 49: My Current Work at SR-FLS

## Slide 50: My Current Work at SR-FLS

## Slide 51: My Current Work at SR-FLS

## Slide 52: My Current Work at SR-FLS

## Slide 53: References
University of Cambridge, Department of Computer Science and Technology, https://www.cl.cam.ac.uk/teaching/2000/AGraphHCI/SMEG/
Les Piegl and Wayne Tiller: The NURBS book, Springer Science & Business Media, 2012
opencascade.com
Mathematical Theory of Gordon Surfaces:
William J Gordon: Spline-blended surface interpolation through curve networks, Journal of Mathematics and Mechanics, pages 931–952, 1969.

## Slide 54: Thank you! ☺

## Slide 55: Degree Elevation
Problem: the B-spline curve or surface shall have a higher degree
Knot vector before:
Knot vector afterwards:
The new control points are computed by evaluating the basis functions at certain parameter values and solving:

## Slide 56: Knot Insertion
Problem: insert knot in the knot vector after the knot with index
New formula of the curve:
The new control points are computed by:
Knot insertion for B-spline surfaces analogue for both knot vectors and